## Slide 1
TRACK 2
The Shadow Wall
Signal Attenuation & the Beer-Lambert Law
Can a digital code survive a shielded partition?
Physics of Electromagnetic Wave Propagation

## Slide 2
THE PROBLEM
Signal Behind a Shielded Partition
Transmitter
I₀
→
WALL
thickness d
→
Receiver
I(z)
?
Key Question: Is the signal intensity after the partition strong enough to decode the digital code?
Attenuation
Signal weakens exponentially as it travels through the medium
Skin Depth (δ)
Characteristic depth at which the signal drops to ~37% of original
Critical Threshold
If partition thickness d > 5δ, signal is physically unrecoverable

## Slide 3
BEER-LAMBERT LAW
The Mathematics of Attenuation
I(z) = I₀ · e^(−αz)
I(z)
Signal intensity at depth z (what the receiver gets)
I₀
Initial signal intensity (what the transmitter sends)
α
Attenuation coefficient of the medium (material property)
z
Distance traveled through the medium (partition thickness d)

## Slide 4
SKIN DEPTH
Calculating δ — The Key Material Parameter
δ = √( 2 / (ωμσ) )
ω
Angular frequency
ω = 2πf (rad/s) — how fast the signal oscillates
μ
Magnetic permeability
μ = μ₀μᵣ — how the material responds to magnetic fields
σ
Electrical conductivity
σ (S/m) — how well the material conducts electricity
Physical meaning: At depth z = δ, the signal intensity has fallen to I₀/e ≈ 36.8% of its original strength

## Slide 5
STEP-BY-STEP SOLUTION
Solving the Shadow Wall Problem
1
Identify Given Parameters
Determine signal frequency f (→ ω = 2πf), material μ and σ from the problem statement
2
Compute Skin Depth δ
δ = √(2 / ωμσ) — This gives you the characteristic attenuation length in meters
3
Find Attenuation Coefficient α
α = 1/δ — The Beer-Lambert coefficient equals the reciprocal of skin depth
4
Calculate Signal at Depth d
I(d) = I₀ · e^(−d/δ) — Substitute the partition thickness d
5
Apply the 5δ Criterion
If d > 5δ, then I(d) < I₀ · e^(−5) ≈ 0.67% of I₀ → signal is physically unrecoverable

## Slide 6
WORKED EXAMPLE
Copper Partition at 1 GHz
Given:
f = 1 GHz → ω = 2π × 10⁹ ≈ 6.28 × 10⁹ rad/s
σ = 5.8 × 10⁷ S/m (copper conductivity)
μ = μ₀ = 4π × 10⁻⁷ H/m (non-magnetic material)
Partition thickness d = 0.5 mm
Calculation:
δ = √( 2 / (6.28×10⁹ × 4π×10⁻⁷ × 5.8×10⁷) ) ≈ 2.09 μm
5δ = 5 × 2.09 μm ≈ 10.45 μm
d = 0.5 mm = 500 μm >> 5δ = 10.45 μm
✗ VERDICT: d ≫ 5δ → The code CANNOT be physically recovered

## Slide 7
PHYSICAL INTUITION
Why Exponential Decay?
Depth z
Intensity I(z)
% Remaining
Status
0
I₀
100%
Full signal
δ
I₀ · e⁻¹
36.8%
One skin depth
2δ
I₀ · e⁻²
13.5%
Two skin depths
3δ
I₀ · e⁻³
5.0%
Three skin depths
5δ
I₀ · e⁻⁵
0.67%
Five skin depths — threshold
10δ
I₀ · e⁻¹⁰
0.005%
Completely attenuated
Each additional skin depth multiplies the remaining signal by e⁻¹ ≈ 0.368 — a geometric shrinkage at every step

## Slide 8
DECODEABILITY CONDITION
The 5δ Threshold Explained
✓ d ≤ 5δ
Signal is RECOVERABLE
• Remaining intensity ≥ 0.67% of I₀
• Sufficient SNR for digital decoding
• Error correction algorithms can recover the code
• Common in practical RF shielding design
✗ d > 5δ
Signal is UNRECOVERABLE
• Remaining intensity < 0.67% of I₀
• Noise overwhelms signal completely
• No error correction can reconstruct data
• Used in Faraday cages for EM isolation
Note: The 5δ criterion is a physics-based hard limit — no amount of signal processing can overcome it

## Slide 9
REAL-WORLD APPLICATIONS
Where Beer-Lambert & Skin Depth Matter
🛡
Faraday Cages
Military & lab shielding designed so d >> 5δ to completely block EM signals. Protects sensitive electronics.
📡
Wireless Comms
Engineers choose frequencies with large skin depth to penetrate building walls and reach receivers inside.
🔬
MRI Machines
RF pulses must penetrate tissue. Skin depth at MRI frequencies determines image slice thickness.
🌊
Submarine Comms
Seawater has high conductivity → tiny skin depth. Only ELF (3-30 Hz) signals reach submarines at depth.
⚡
Power Cables
At 50/60 Hz AC, skin effect forces current to the conductor surface — drives cable design choices.
🔐
Secure Rooms (SCIFs)
Sensitive Compartmented Info Facilities use thick copper shielding to prevent data leakage via EM radiation.

## Slide 10
KEY TAKEAWAYS
The Shadow Wall — Summary
01
Beer-Lambert Law
I(z) = I₀e^(−αz) governs how any wave or signal attenuates exponentially through a medium
02
Skin Depth Formula
δ = √(2/ωμσ) — depends on frequency and material; smaller δ = more attenuation
03
Attenuation Coefficient
α = 1/δ — directly ties Beer-Lambert to skin depth physics
04
The 5δ Rule
If partition thickness d > 5δ, signal intensity < 0.67% of I₀ → code cannot be recovered
05
Design Insight
Increasing frequency or conductivity reduces δ — making shielding more effective at smaller thicknesses